## Slide 1: INTRODUCTION
19AIE104 Introduction to Electrical Engineering
Submission mode:
Group, Recording

## Slide 2
DC GENERATOR
Q1)
For the DC generator with specification as below, analyze and comment on the relationship between the following parameters:-
Rating -- 200 V, 1500 RPM
4 Poles, 50 mWb
Assume that EMF generated is available at the output
Generated EMF and Magnetic flux intensity
Generated EMF and Speed of rotation
Magnetic Flux and Speed of rotation
Prove your analysis with respective plots. Submit the supporting files used for plotting.
While assessing the inter-dependence of parameters, consider the remaining parameters if any, to be constants.
Analyze

## Slide 3: DC GENERATOR
Q2
The magnetic flux and the rotating speed of a DC generator is changed relative to each other such that the generated voltage is constant. The range of variation of flux is 5 to 10mWb and that of speed is 1000 to 1500 RPM. If the generated voltage is 250 V at 1500 RPM and 5mWb, plot the flux vs speed characteristics.
Apply
Q2a
In Q2, if the flux is maintained constant at 8 mWb, plot the EMF generated vs speed characteristics.
Q2b
In Q2, for a feasible constant speed of rotation of your choice, plot the EMF vs flux characteristics.
Use MATLAB/Octave for plotting.

## Slide 4: DC GENERATOR
Q3
A DC generator is to be constructed with armature winding of resistance and field winding of . The generator output voltage is supposed to be stable at 220 V while supplying a load of 2.2 kW alongside powering up the field winding.
Design
Q3a
With the above information, decide which type of DC generator construction is suitable for this application. Make logical assumptions…
Q3b
Plot the V-I characteristics for the opted generator model, if the load current varies from 0 to 10 A.
Use MATLAB/Octave for plotting.