## Slide 1: Assignment:19AIE104 Introduction to Electrical Engineering
SUBMITTED BY GROUP 19
Names of Group members :
1.VIGNESH M. [1008496 ]
2.VIKHYAT BANSAL [1007359]
3. YARRAM SRI SATHWIK REDDY [1038833]
4.AMAN SIROHI [1042496]

## Slide 2
Q1) PART 1: Assume a random value of your choice for resistance (10-10K Ω). Plot the characteristics given below. The resistance coefficient of temperature is 0.02 Ω/°c, and the voltage range is 0-240 V.
• Voltage - Current
FORMULA EXPLANATION :
Relation between current and voltage is expressed as I=V/R
V= voltage, I= current, R= resistance
Let us assume R= 100 for this question

## Slide 4
• Power-Voltage
FORMULA EXPLANATION :
Relation between power and voltage is expressed as P= R*(I^2)
By using V=IR relation, we get that
P=(V^2)/R
V= voltage, P= power, R= resistance
Let us assume R= 100 for this question

## Slide 6
• Power-Current
FORMULA EXPLANATION :
Relation between power and voltage is expressed as P= R*(I^2).
V= voltage, P= power, R= resistance
Let us assume R= 100 for this question

## Slide 8
PART 2: Due to prolonged operation, the temperature of the resistance rises by 10°c. Replot the above considering the new scenario
FORMULA EXPLANATION:
R1 = R * ( 1 + A* (T) )
Here,
R1= new effective resistance
A= thermal coefficient of the given conductor
T= change in temperature
R= initial resistance

## Slide 9
• Voltage-Current
FORMULA EXPLANATION :
Relation between current and voltage is expressed as I=V/R1
V= voltage, I= current, R1= new effective resistance
We know from our last calculation R1=120Ω

## Slide 11
• Power-Voltage
FORMULA EXPLANATION :​
Relation between power and voltage is expressed as P= R1*(I^2)​
​
By using V= I*R1 relation, we get that​
​
P=(V^2)/R​1
​
V= voltage, P= power, R1= new effective resistance​
​
We know from our last calculation R1=120Ω

## Slide 13
• Power-Current
FORMULA EXPLANATION :​
Relation between power and voltage is expressed as P= R1*(I^2).​
​
V= voltage, P= power, R1= new effective resistance​
​
We know from our last calculation R1=120Ω

## Slide 15: 2) Solve the circuits using mesh or nodal network matrices .
A)
We first obtain the mesh currents using KVL.
(*Kirchhoff's Voltage Law)
*KVL(Sum of the voltage difference around any closed loop in
a circuit must be zero)
For mesh 1, Here i0 = (i1-i2)
-24 + 10(i1 -i2) +12(i1 -i3) = 0
11(i1) - 5i2 – 6i3 = 12 ------(1)

## Slide 16
For mesh 2:
24i2 + 4(i2 -i3) +10(i2 -i1)
-5i1 +19i2 – 2i3 = 0 ----------(2)
For mesh 3:
4I0+ 12(i3 - i1) + 4(i3 - i2) = 0
But here I0 = (i1 -i2)
4(i1 - i2) +12(i3 - i1) + 4(i3 - i2) = 0
-i1 –i2 + 2i3 = 0 ------------(3)

## Slide 17
Solving equations 1,2 and 3 to get i1 , i2 and I0 Solving by matrix method using octave /Matlab
* i1 = 2.25 * I0 = i1 - i2
* i2 = 0.75 = 1.5
* i3 = 1.50

## Slide 18
B)
By using Nodal analysis
* Assume that the currents
i1 ,i2 ,i3 is flowing in the
Directions as shown in fig:
* Apply KCL at Nodes v1, v2,v3
* KCL (Summation of current entering at
Node = Summation of the current leaving
the node)
* KCL at node v1:
3 = ix + i3 {* Higher voltage – lower voltage}
v1 –v2 v1 – v3
3 = --------- + ----------- {*multiply by 4 on both sides}
2 4
12 = 3v1 – 2v2 –v3 ------(1)

## Slide 19
* KCL at node v2:
ix = i1 + i2 {* Higher voltage – lower voltage}
v1 - v2 v2 v2 -v3
----- = ------- +---------- {*multiply 8 on both sides}
2 4 8
4v1 – 4v2 = 3v2 - v3
4v1 –7v2 + v3 =0 ------(2)
--------------------------------------------------------------------------
* KCL at node v3:
2ix = i2 + i3
2(v1 - v2) v2 – v3 v1 – v3
------------ = ---------- + -----------(Mul by 8 on b.s)
2 8 4
8v1 – 8v2 = v2 –v 3 + 2v1 -2v3
6v1 – 9v2 +3v3 = 0 -------(3)

## Slide 20
*Solving by matrix method using Matlab/octave *Solving using linear equations:
* v1 = 4.8
* v2 = 2.4
* v3 = -2.4
* ix = v1 –v2/2
* ix = 1.2

## Slide 21
Q3.1.Construct the circuit described by the data given in Table.
From basic knowledge of Circuits we can create a circuit based on following data:-

## Slide 22
Q3.2 Create the mesh/nodal network matrix for the circuit.
Writing Equation for above circuit will give us:- Loop1 -10i1-30(i1-i2)-20i1=0 Loop 2
-40i2-60(i2-i3)-50i2-30(i2-i1)=0
Loop 3
-70i3-80i3-90i3-60(i3-i2)=0
AFTER SOLVING FURTHER WE GET,
-60i1+30i2 = 0 - Eqn1
-180i2+30i1+60i3 = 0 - Eqn2
-300i3+60i2 = 0 - Eqn 3

## Slide 23
From three equations we get our matrix,
CREATING MATRIX USING MATLAB:- CODE FOR THE SAME ----------------------------------
Final current will be zero in each loop will be zero
i1=0
i2=0
i3=0

## Slide 24: Q3.3.If the circuit is excited by a 100 V DC, write the MATLAB/Python code to solve the systems of equations in (2).
Writing Equation for given circuit using mesh analysis:
Loop 1
100-10i1-30(i1-i2)-20i1 = 0
Loop 2
-40i2-60(i2-i3)-50i2-30(i2-i1) = 0
Loop 3
-70i3-80i3-90i3-60(i3-i2) = 0
After Solving further we get,
100-60i1+30i2 = 0 -Eqn1
30i1-180i2+60i3 = 0 -Eqn2
-300i3+60i2 = 0 -Eqn3

## Slide 25
From help of given image on right we will create
MATRIX in MATLAB:-
i1=1.8301
i2=0.3268
i3=0.0654
From three equations we get our matrix,
CREATING MATRIX USING MATLAB:-
CODE FOR THE SAME ----------------------------------

## Slide 26
Q4.
1. Formulate the network equations to demonstrate the transient operation of a parallel RLC circuit without EMF excitation.
2. Using MATLAB/Python, plot the transient nature of the current in a parallel RLC circuit without excitation. Provided C = 0.05, L = 0.55, R = 0 and the capacitor is charged to 8V in the beginning.
3. If a series RLC circuit (C = 0.05, L = 0.51, R = 0.15) is being excited by a step input signal of 10 V, {𝑉𝑠 0 = 0 𝑉, 𝑉𝑠 0 + Δ𝑡 𝑡𝑜 𝛼 = 10 𝑉}, plot the transient response using MATLAB/Python.

## Slide 27
Ans 4.1

## Slide 28
Ans 4.2

## Slide 30
Ans 4.3

## Slide 31
THANK YOU